## Slide 1: Biology at SWING beamline
A. Thureau, T. Bizien, J. Pérez, Y. Liatimi
Synchrotron Soleil, Gif-sur-Yvette, France
SWING
SAXS - WAXS - GISAXS

## Slide 2
X-Ray Beam
Users environment
In vacuum detector
(from 500 to 6700 mm sample to detector distance)
Full flux = 5.1012 ph/s @ 12 keV
Beam size (FWHM) =
400 (H) x 25-100 (V) µm2
Structural Biology (macromolecular shapes / low resolution structure)
Soft Condensed Matter (crystal growth, colloids, polymers, liquid crystals, hierarchical systems, …)

## Slide 3
  Thermostated Anton Paar Rheometer (collab. LPS, Orsay, France)
  Biologic SFM400 Stopped-Flow for chemistry/biology (courtesy Biology Lab)
  Linkam Hot stage for capillaries (T < 600°C)
  Circulation cell for proteins in solution, with Peltier T° control & UV-Vis Abs
  On-line HPLC coupled with preparator and injector for protein solution samples
Many available sample environments
*Interchangeable* sample holders:
Motorized (3 axis), Thermalized (10 – 70°C)
Flow-through thin (10µm) quartz capillaries
For gels
For sealed capillaries
  Automated High Pressure Cell for liquid samples (P < 5 kBar)
  Automated Injection Robot for liquid samples

## Slide 4
SEC-SAXS
  UV-SAXS+UV-MALLS-RI installed permanently
IspyB
  AutoBioSAXS is working and connected to IspyB
  Confidentiality of BAGs
What I'm going to talk about

## Slide 5
Bio-SAXS schematics
Samples for SEC-SAXS: 10µl (20mg/ml) to 80 µl for (1,0mg/ml)
UV detector
(8 wavelengths)
MALLS detector
(18 angles+QELS)
RI detector
Automated process for injection and detection:
Automated injection for both Batch and SEC-SAXS
Users just need to set up : Sample name, Rack Position, Volume and Column circuit
Multiple injections for both Batch and SEC-SAXS can be set-up
Automated analysis process: AutoBioSaxs + IspyB
Saxs Curves => In-House & Atsas pipeline
Samples for BATCH-SAXS: 10µl (1 mg/ml) to 50 µl for (0.1 mg/ml)
SAXS

## Slide 6
HPLC – MALLS/QELS – SAXS – RI online
Wyatt 18-angles MALLS/DLS
Wyatt Refractometer
Agilent UV
SAXS + UV
Switches for easy circuit purge
New Batch Mode Injector
Capillary cleaning automated set-up
Old Batch Mode Injector
=> MALS & RI : new possible informations for IspyB

## Slide 7: AutoBioSAXS : Automatic Data Treatment workflow for BioSaxs
I0, l
Detected : I(Q)
2θ
2D detector
Ln ( I )
Q=4π sinθ/λ
Radial average
+
buffer subtraction
(Foxtrot libraries)
(ATSAS suite of programs)
SAXS coupled with Size Exclusion HPLC
(IspyB Web Application)
(IspyB Web Application)

## Slide 8
Implementation of confidentiality of BAGs on SWING Beamline
BAG
<project ID>
PI Member A <member ID>
PI Member C <member ID>
PI Member B <member ID>
Session 1 <session ID>
Session 3 <session ID>
Session 2 <session ID>
User 1 => <project ID> / <Member ID> / <Session ID>
User 3 => <project ID> / <Member ID> / <Session ID>
<project ID> / <Member ID> / <Session ID>
<project ID> / <Member ID> / <Session ID>
Sample Z
Sample X
User 2 => <project ID> / <Member ID> / <Session ID>
<project ID> / <Member ID> / <Session ID>
Sample Y
User 1
User 2
User 3
Sunset
IspyB
Pre-Experiment
Experiment
Post-Experiment
Sunset
Swing

## Slide 9
experimental
Dadimodo: refining domain orientations with an all-atom description
Initial (slow) version : Evrard et al. (2011), J. Appl. Cryst., 44:1264-1271.
Parallel implementation of the genetic algorithm
  7300 Atoms  7 hours on a 20 processor node
User-friendly input
  User-defined topology : Pdb file + rigid bodies definitions
  Automated completion (when needed) of pdb input files
This year
  Server dedicated to external users
Dadimodo
O. Roudenko , A. Thureau, J. Pérez
=> Why not also on IspyB ?

## Slide 10
MEMPROT : Correlations between parameters in the corona geometrical model
Pérez J. & Koutsioubas, A. Acta Cryst. (2014)
DeltaHasR-HasA shape
=> Why not also on IspyB ?

## Slide 11
HasR-HasA, now including the signal domain
Dadimodo  specially adapted for coarse grain corona
Average position in presence of HasA
Average position in the absence of HasA
The interaction of HasA with HasR seems to bring the signaling domain closer to the membrane
Wojtowicz et al., Biochem. J. (2016) 473, 2239–2248
=> Why not also on IspyB ?

## Slide 12
To resume, on Swing Beamline:
Saxs Measurement
AutoBioSaxs
IspyB Database
Users
Simple Project & BAGs (confidentiality)
IspyB via Sunset
IspyB Test Database
Soleil Staff
EXI (direct access)
Just some ideas to add more data on IspyB
Mals, RI & fluoresence profils curves
Membrane proteins (EMBL-HH)
Atomic models
EXI via Sunset
In few weeks
EXI development to be done by Soleil
Modification of IHM
Including ESRF request
Reprocessing
…

## Slide 13
Contributors
  AutoBioSAXS – Foxtrot - IspyB
      Majid Ounsy (ICA)
      Grégory Viguier (ICA)
      Idrissou Chado (ISG)
      Raphaël Girardot (ICA)
      Frantz Pili (ICA)
      Alejandro Diaz (ISI)
  HPLC-MALLS
      Mattia Rocco
  Memprot
    Alexandros Koutsioumpas
    Maciej Baranowski
  New BioSaxs cell
    Cedric Dicko (Lund University)
    Tomás Plivelic (Max IV)
    Jean-Michel Dubuisson (BE)
    Matthieu Lecroard (BE)
  Dadimodo on the Web
    Olga Roudenko (ICL)
    Nicolas Labrude (ISG)